## Slide 1: Automated PIN Cracking
R2B2 and C3B0
Justin Engler Paul Vines
Senior Security Engineer Security Engineering Intern

## Slide 2: Agenda
Current PIN Cracking Methods
Cracking with Robots
R2B2
C3BO
Defeating the Robots

## Slide 3: PINs
One of the most popular ways to lock mobile devices
  Commonly still only 4-digit despite ability to be longer
  User chosen, so typically low-entropy
play.google.com

## Slide 4: PIN Cracking Now
Jailbreak and Crack
Keyboard Emulation
Brute Force the UI

## Slide 5: PIN Cracking Now
Jailbreak and Crack
Keyboard Emulation
Brute Force the UI
Punish an Intern

## Slide 6: Punish an Intern
Forcing your intern to try all 10,000 4-digit combinations will surely be more productive than anything else they could have been doing, except maybe getting coffee
Problem: Interns are universally bad at their jobs, so they might miss some of the combinations

## Slide 7: PIN Cracking with Robots
Required Abilities:
  “Push” buttons in sequence
  Remember what buttons were pushed
  Recognize success
    Not always necessary

## Slide 8: Delta Robot
Designed for fast precision industrial work
Simple combination of 3 single-motor arms gives precision 3D movement with somewhat small range of motion
Fairly simple motion control
*
* Lopez, Castillo, Garcia, and Bashir. Delta robot: inverse, direct, and intermediate Jacobians. Proc. IMechE Vol.220(2006)

## Slide 9: Still a lot of maths…

## Slide 10: Still a lot of maths…

## Slide 11: Robotic Reconfigurable Button Basher
Arduino microcontroller
3-d printed parts
Open source code and design for a delta robot by Dan Royer (marginallyclever.com)
  Uses serial port communication to control the movement of the robot
Available as a kit, or DIY

## Slide 12: Modifications
The original delta robot kit was modified to have its tool be a touch-screen stylus tip for pressing buttons
  Important: Stylus tip needs to be grounded
A camera was added to allow easier user interface with the robot to set up the PIN cracking task
  And recognize when the device is unlocked!
The motion control software was modified to speed up movement, up to 5 presses/second

## Slide 13: Wrap Everything in Python
Controls the robot movement through the serial port
Performs image analysis of the camera feed
Provides a simple interface for the user to set the robot up for PIN cracking
Detects success of PIN cracking to stop robot and alert user

## Slide 14: Capacitive Cartesian Coordinate Bruteforcing Overlay (C3BO)
Attach a grid of electrodes to the device’s virtual keyboard
Trigger electrodes via an Arduino to trick the device into thinking the screen was touched at that point
Faster, Better, Cheaper (~$50)

## Slide 15: C3BO :(
Doesn’t work.

## Slide 16: (a bit) Better than brute-forcing
Harvested 4-digit sequences from online password lists
  (eharmony, myspace, etc.)
  Presumably what Nick Berry did for his blog but wouldn’t share…
Combined with Daniel Amitay’s (danielamitay.com) phone app PIN list

## Slide 17
Chart: # of PINs tried

## Slide 18: Real Buttons Too!
R2B2 can of course also be used for brute-force PIN cracking of physical buttons as well
Electronic keypads or completely mechanical keys, provided it can detect when it has succeeded

## Slide 19: Defeating the Robots
Forced delay timer after X attempts
  On Android this is 30 seconds regardless of previous attempts
    R2B2 would succeed in a worst case of ~20 hours
    Likely success much sooner (80 mins =50%, 7 hrs =80%)
User Lockout after X attempts
  On iOS, 1 minute lockout after 5 guesses
    Lockout time quickly scales up for continued bad guesses (1 minute, 5 minutes, 15 minutes, 60 minutes)
    Roughly 20% success rate on a 20 hour run

## Slide 20: Robots > Apps
Lots of apps to replace lock screen or provide additional “protection” to elements of the phone (media storage etc.)
Tried 13:
  4 had lockouts of >= 5 minutes/5 attempts
  9 had no lockout at all

## Slide 21: Defeating the Robots For Users
PIN character set and length | 1 PIN per second | 1 PIN per second, plus 30 seconds every 5 guesses
3 Digits | 16 Minutes | 117 Minutes
4 Digits | 167 Minutes | 19.4 Hours
5 Digits | 27 Hours | 8.1 Days
6 Digits | 11.8 Days | 81 Days
4 Lowercase + Digits | 19.4 Days | 136 Days
7 Lowercase + Digits | 2484 Years | 7.83e10 Centuries
4 Printable ASCII (94) | 2.48 Years | 7.81e7 Centuries
7 Printable ASCII (94) | 20563 Centuries | 6.48e13 Centuries

## Slide 22: Acknowledgments
Thanks to iSEC Partners and the NCC Group for supporting this research
Thanks to Dan Royer for providing the motion control code and robot build plans
Thanks to Daniel Amitay for parts of our PIN data
Thanks to David Nichols for analyzing the PIN using apps

## Slide 23: Contact Information
Justin Engler
  @justinengler
Paul Vines
  plvines@uw.edu